## Slide 1: Veoneer PFMEA Go, See & Fix Workshop for suppliers

## Slide 2: Content of Presentation
In this presentation you should be able to understand:
    What a PFMEA Go, See & Fix Workshop is
    When a PFMEA Go, See & Fix Should be Done
    How to Perform a PFMEA Go, See & Fix Workshop
    How to Prepare for the Workshop
    What Documents / Checklists are Required
    How to Record Workshop Results

## Slide 3: Introduction
PFMEA Go, See and Fix is a tool when used correctly, helps identify potential failure modes within any process. This in turn guides improvement while reducing exposure to risk.
What is PFMEA Go, See & Fix:
  A tool for discovering potential failure modes before they occur
  A method for strengthening PFMEA’s so past history is not repeated
  A method for ensuring all of our production documents are congruent
  A tool to check that process changes haven’t created potential problems
  A method for making our processes more robust
  A tool for prevention of non-conforming material
  A tool for reducing scrap
  A way of strengthening teamwork
  A continuous process

## Slide 4: Introduction
What it is not:
  Not - a new technology, rocket science or new tool
  Not - an audit
  Not - an activity to be performed in the office or conference room
  Not - a tool to point at or blame others
  Not - a tool to break machines
  Not - a “Check the Box” requirement
  Not - a One Time event

## Slide 5
When should Go, See & Fix PFMEA be done?
PFMEA Go, See & Fix Activity
To be done on new equipment.
On existing equipment & processes for continuous quality improvement.
Following line transfers and relocations:
  • From one plant to another or within the plant.
Following any process changes.
Project
Planning
Concept Definition
Product & Process Development
Product & Process Validation
Serial Production all processes
Product Launch

## Slide 6: Workshop Preparation
Select a dedicated time frame for activity
  Weekly, Semi-weekly- 1 hour, 2 hours
        Note: To complete a process will probably require many weekly activities. Do as much as can be completed in the scheduled time,
        clean up the area and prepare to begin at this point the following week
Choose a Process / Machine to perform the activity on
Choose a part number for the activity

## Slide 7: Workshop Preparation
Form a strong Cross Functional Team (4 - 7 Persons)
  Team should consist of at least the following
  Team Leader- Either Process Engineer or Quality Engineer seems to work best
  Process Engineer (If not the leader)
  Quality Engineer (If not the leader)
  Production Supervisor
  Production Associate
  Maintenance Technician
Include people not involved with the process (Fresh Eyes Approach)
Cont.

## Slide 8: Documentation Preparation
Gather a copy of all applicable documents for chosen process.
  Applicable Part Drawing(s)
  Process Flow
  Process FMEA
  Control Plan
  Standard Work Instructions
  PFMEA Go, See & Fix Document
  Machine Preventative Maintenance Instructions.
  Any Customer Special Requirements
  Previous Customer Claims

## Slide 9: Documentation Preparation
Choose a location to review documents
  Office
  Training Room
  Team Table
cont.

## Slide 10: The Documentation Comparison Process
Compare the Documents from slide 8 for chosen process
  Insure all Special Characteristics (SC’s and CC’s) from Drawing are carried down to supporting documents
    SC’s & CC’s in PFMEA have Process Controls that are Poka-Yoke’d or 100% detected and these are validated regularly on the Control Plan
  Process Number matches for all documents
  Control methods listed in PFMEA are reflected in Control Plan and / or Work Instructions
  Verify PM’s listed as Prevention / Detection Controls do exist
  PFMEA Severity ratings comply to Veoneer Standard VS-104
  Note any discrepancies so that the documents can be updated

## Slide 11: The Worksite Process
Move the Activity to the Process being reviewed (Gemba)
  Take all reviewed documents
  Take all Team Members
Observe all Safety Requirements - Always!
Compare PFMEA to Process
  Does the PFMEA reflect exactly what the process does
Compare Machine limits to the Drawing limits
  Verify limits and adjustments cannot be made by unauthorized personnel
Ensure Sensors are programmed with “Change of State” requirement.
  Test / Verify the Sensors for “Change of State”

## Slide 12: The Worksite Process
Verify validation parts comply to standards
  MVP’s (Master Verification Part), Golden Samples, Red Rabbits, etc.
Verify Control Plan and Work Instructions contain the following:
  Correct Scrap / Reject / Incomplete part reaction plan
  Correct Poka-Yoke Verification frequency and instructions
  Proper Measurement devices. Compare to what is actually used
    How to perform measurement
  Correct Visual Aides available where Visual Inspection is required
cont.

## Slide 13: The Worksite Process
Attempt to build a bad part
  Be relentless during this portion of the activity
    Remember, you’re attempting to understand if it is possible
    Regardless how remote the possibility, if it’s possible, someday it will happen
    Protect your company and your customers
cont.

## Slide 14: The Worksite Process
Attempt to build bad parts.
Use the PFMEA Go, See and Fix Template and the following slides for ideas & possible ways to build / process bad parts at the selected process. The following sections of the template are methods to help complete this
  Section 2-1
  Section 3-4
Section 3-5
Section 3-6
Section 4-1
Section 5-1
Section 6-1
Section 8-1
Use Production Operator & Maintenance knowledge for other potential ways to create an abnormal situation
cont.

## Slide 15: More Failure Mode & Effect Questions
For mechanical motions:
What happens if:
Motion does not occur?
Motion is incomplete or too short/long?
Motion exceeds normal travel?
Motion is too fast/slow?
Force/Torque is too low/high?
Part sticks to moving machine component?
Contacting components are worn or damaged?
Too much/little lubricant is present at process?
For mechanical motions:
What happens if:
Crimp is too deep/shallow ?
Crimp is misaligned?
A Crimp Jaw breaks?
Process parameters are incorrect (jaws, pressure, etc..)
For welds:
What happens if:
Current is too high/low?
Weld time is too long/short?
RPM is too high/low (inertia weld)?
Pressure is too high/low (inertia weld)?
Shield gas flow is too high/low?
Weld is misaligned?

## Slide 16: More Failure Mode & Effect Questions
For Preventive Maintenance:
What happens if:
Tool being used exceeds Tool Life cycles?
PM not performed within the scheduled time/cycles?
Post Repairs are not systemically re-qualified?
Replacement tool details do not have a unique ID, linked to dimensional verification prior to make available for use?
PM Schedule not adjusted based on actual time/cycles to failure?
PM Task checklist does not account for issues observed?
For manual or automated part placement:
What happens if:
Part is not seated?
Part is not properly oriented?
Part is upside down?
Part or component is missing?
More than required quantity installed?
Part or nest tooling is worn or broken?
Chip/contamination is present at nest/part?
Non-compliant Nest Tooling is installed?
For inspection:
What happens if:
Fails to detect a bad part?
Fails to accept a good part?
Equipment is not calibrated/verified properly?
For inspection:
What happens if:
Part is dropped?
Part skips operation?
Part is processed more than once?
Nonconforming part is not contained?
cont.

## Slide 17: The Worksite Process
  Document all discovered Failure Modes and all Potential Causes
    Note: Items affecting a special characteristic or having significant impact on product, need to be addressed immediately to prevent risk of shipping Non-Conforming Product
  Determine if bad parts will be detected later in the process or during another process
  Verify the detection with a bad part
cont.

## Slide 18: PFMEA Go, See & Fix Activity Completion
Remove all material from the process that was used during the activity and place equipment back to normal operating condition
Create Action List to correct all discoveries
Assign responsible individuals to each action
Update all affected documents from each improvement
Congratulate the team

## Slide 19: Next Step
Choose another process
  Remember, this a continuous process.

## Slide 20: Thank You!