## Slide 1: Production Trial Run Capacity Report Training
Veoneer Supplier Manual (VSM)

## Slide 2: Production Trial Run Capacity Report
Purpose
  The primary purpose of the Production Trial Run Capacity report is to confirm the
  installed capacity during the different production trial runs.
  The secondary purpose is to measure the efficiency of the Supplier process
  considering the following factors:
    and confirm the agreed installed capacity during both RFQ phase and Contract
    Review
  3. This template will also allow to track all issues identified and the progress done
  during the different production trial runs. Issues will be tracked in the sheet
  “Problem follow-up sheet” and should be closed at Run @ Rate at the latest.
  Equipment availability
  Performance efficiency
  Quality Rate

## Slide 3: Production Trial Run Capacity Report
Overall view- Sections in the template
Calculated field
SECTION 1
SECTION 3 (informative)
SECTION 2

## Slide 4: Production Trial Run Capacity Report
Section 1
% machine time Percent of machine/process time dedicated to this part.
Max week demand (w/safety)
Maximum weekly demand to cover temporary peak demands. This information should match what is agreed in the Cost Breakdown and Contract Review.
Regular + 20%.
Bottleneck OEE (%) :
See OEE color definition below. Lower OEE indicates higher potential to affect capacity, quality, or cost and should be investigated for potential improvements.
Reg week demand
Regular weekly demand
Shifts per day Regular number of shifts per day.
Effective hours/shift (minus breaks) Example: if during a 8 hours shift, we have three breaks of 20 minutes, effective hours per shift will be: 8 hours - (60 min/60) = 7 hours
Workdays per week reg Regular number of workdays per week.
Workdays per week max Maximum number of workdays per week to temporarily cover peak demands. This is for information only, is not used in calculations on this sheet.
Available regular hours/week Available hours-week= regular shifts per week x effective hours per shift.
(% machine time x effective hours per shift x regular workdays per week x # shifts per day) - (# runs per week x set-up hours per run).
(E4xE8xE9xG8)-(G4xH4/60)
Example (.5x7x5x2)-(3x20/60) = 35-1 = 34
Target 'OK' PPH Target OK PPH (Part per Hour)=
Maximum weekly capacity / available regular hours per week for this product. G7/E10. Example 18000/34 = 529.
# runs/week How many times this part will be run per week on average.
Set-up minutes How many minutes to set-up (changeover) to this part.

## Slide 5: Production Trial Run Capacity Report
Section 2
Calculated field
PRODUCTION RUN
Please state the type of Production Run:
- First Production Trial
- PPAP Production Trial
- Run @ Rate
SET-UP TIME (Minutes) This is the time needed to put the process in conditions to start the production trial, yellow indicates setup for trial took longer than normal (compared to set-up minutes shown above).
ACTUAL 'OK' PPH calculated field = (Number of good parts/time x 60).
First row example: J16/H16*60 =
2000 Good parts/240 minutes x 60 minutes/hour = 500 PPH.
Counter measures identified For any judgement less than 100%, countermeasures must be identified on Problem Follow-up Sheet.
ACTUAL CYCLE TIME (Seconds) Cycle time Actual per part (seconds) = Time (min) x 60 / Number Parts Produced..
BOTTLE-NECK? Is this the bottleneck (slowest) operation as defined above?
CAPACITY JUDGEMENT Compares quoted (expected) OEE to trial run OEE, factors in lowest one for bottleneck operations. Also compares quoted set-up time to trial run set-up time, factors in highest one (see Adjusted target OK PPH in column Y). See bottom of sheet for color definition.
QUOTED PROCESS SCRAP (%) From Supplier Cost Breakdown. To be referred to in the contract review. For information only, not used in calculations.
TR OEE JUDGEMENT The Trial Run Overall Equipment Effectiveness measures how effectively the process was utilized during the trial run, which has an effect on capacity. OEE = Equipment availability x Performance efficiency x Quality rate during the trial run.
ACTUAL (Minutes) Number of stoppages during the Production Run. For information only.
Nb. STOPPAGES Number of stoppages during the Production Run. For information only.
ACTUAL SCRAP (%) (Number of parts produced - Number of Good parts) / Number of parts produced.
IDEAL OR QUOTED CYCLE TIME (Sec) From supplier cost breakdown, to be referred to in the contract review. It refers to the ideal (best possible) cycle time per part. The cell will turn yellow if quoted (ideal) cycle is time longer than the actual cycle time, which should not happen.

## Slide 6: Production Trial Run Capacity Report
Section 3

## Slide 7: Production Trial Run Capacity Report
Formulas (1/2)
CAPACITY (TRIAL RUN)
Target “OK” PPH (Part Per Hour) = ------------------------------------------------------------------
Available Regular Hours per week for this product
Time (min)
Actual “OK” PPH (Part Per Hour) = --------------------------------------------------- X 60
Number of good parts
Regular capacity / available
Capacity Judgement (%) = ---------------------------
Number of parts produced
Target “OK” PPT
EFFICIENCY (QUALITY )
Actual scrap (%) = ---------------------------------------------------------------------
Actual “OK” PPT
Number of parts produced- Number of good parts
EFFICIENCY (CYCLE TIME )
Actual (sec) = ----------------------------------------------------------------
( Time (min) Equipment downtime (min) x 60
Number of parts produced

## Slide 8: Production Trial Run Capacity Report
Quality rate (%) = ----------------------------------------------------------------
Performance efficiency (%) = ------------------------------------------------------------------
Equipment availability (%) = --------------------------------------------------------------
Formulas (2/2)
EFFICIENCY
Time (min) –Equipment Downtime Actual (min )
Time (min)
Number of good parts
Quoted Cycle time (sec)
Cycle time actual (sec)
  Actual TR (Trial Run) OEE = Equipment availability x Performance efficiency x Quality Rate
Number of parts produced

## Slide 9: Production Trial Run Capacity Report
Problem follow up sheet

## Slide 10: Thank You!