## Slide 1: TFC Training
Overview
Template details

## Slide 2: TFC Training
Overview

## Slide 3: Executive Summary – TFC Process
Standard: No standard. Defined in VSPP and Part of VS100 Tasks
Responsibility of: Purchasing and SQ
Purpose: To secure component feasibility in manufacturability, quality, packaging definition and timing
Why: It is an important tool to minimize any risk associated with the launch of new components.
What TFC need to do: Understand the basics and importance of TFC. To make sure that issues identified during the TFC are addressed properly and on time by the cross-functional team.
Project Risk due to non-compliance: Delays and Quality issues (NCMs and Cat A)
Notes: Here is a top level summary of the TFC process.
The TFC process is defined in the VSPP and is a task in VS100.
It is a cross functional team activity but the Primary responsibility is with Purchasing or the SQ depending on the phase, which will be discussed later.
As I have already mentioned the Purpose is to reduce risk of supplied component launch by reviewing the component design for manufacturability, Quality, that the part packaging is acceptable and that component launch timing can be met.
If any issues are identified then a reaction plan must be established and agreed upon by the supplier and Veoneer.
Doing this will help eliminate project delays and quality issues that result in NCMs, Category A events and or customer missed timing.

## Slide 4: VSPP
Submodule 3.2 TFC Process
# | Sub-Module | Purpose
3.2 | TFC Process | To secure component feasibility in manufacturability, quality, packaging definition and timing
3.2 Team Feasibility Committment
3.2.1 TFC
(Sourcing Phase)
3.2.2 TFC
(Tool Order Phase)
3.2.3 TFC
(SQP/PPAP Phase)
3.2.4 TFC
(Serial Phase)
Process Owner
Project Buyer (Sourcing and Tool Order phase) Project SQ (PPAP Phase)
# | TFC Phases | Deliverables
3.2.1 | TFC (Sourcing Phase) | Identify a supplier that meets requirements with no show stoppers which is OK for sourcing
3.2.2 | TFC (Tool Order Phase) | Get the commitment from the supplier and Veoneer cross functional team regarding feasibility in manufacturability, quality, packaging definition and timing in order to minimize any risk and cost avoidance upfront.
3.2.3 | TFC (SQP/PPAP Phase) | Complete all agreed actions to obtain Full PPAP Approval.
3.2.4 | TFC (Serial Phase) | Similar as previous three steps but a serial phase.
Notes: The TFC process has been divided into four phases.
The first is the Sourcing phase. This phase helps us identify a supplier that meets requirements with no show stoppers that is good for sourcing.
The second phase is the Tool Order Phase. In this phase we identify and agree on actions for each issue identified.
The third phase is the SQP Phase. This phase requires that all agreed actions are completed to obtain full PPAP approval.
The fourth Phase is a phase for changes during serial production. It combines the applicable steps of the three previous phases for serial life changes.

## Slide 5: TFC Participants
Veoneer – Project Buyer
Veoneer - Project SQ
Veoneer - Engineer (D or E)
Supplier - Representative(s)
(covering functions: Engineering, Tooling,
Quality, Account Management, Sales)
Veoneer – Project Manager
Veoneer – Tool Engineer
Veoneer – Logistics
Veoneer – Industrial Engineer
Veoneer – Project Quality Engineer
Veoneer – Raw Material Expert
Supplier – Tool Maker
Supplier – Logistics
Participant
Support (if necessary)
Notes: Required participants include:
Project Buyer
Project SQ
D or E Engineer
And supplier representatives that represent the following functions engineering, tooling, quality, account management and sales.
You can also see the list of other functions that can be invited to participate as required. It is highly recommended that the Program Manager participate to understand risk to their project, help drive action and provide resources.

## Slide 6: TFC template
Notes: Here is a screenshot of the TFC template filled out. Also shown is the checklist that the supplier is to evaluate the component against for feasibility.
Key items for the template.
Veoneer should provide the key timing dates such as tool order, first off parts, PPAP submission and Veoneer SOP (the supplier can get these dates from the RFQ) However, First off Part, PPAP submission and Veoneer SOP are automatically populated in the TFC template from the E-sourcing RFQ.
Suppliers are not required to review in detail the checklist during the Sourcing phase but must review in the Tool order phase.
The supplier must make a declaration of whether the design is feasible to PPAP without any deviations. They must also make a declaration that the design has been evaluated against the Checklist cririta.
Each issue identified by the supplier should have a recommended action and the status changed to proposed. Once the Detailed review meeting is held and agreement of actions made between Veoneer and the supplier the status should be changed to Agreed. Upon completion of actions the status is to be changed to Complete.

## Slide 7: TFC flow chart
TFC meeting / call
supplier & Veoneer
Tool order /
order of design change
TFC follow up
TFC closure meeting/ call with supplier
Supplier fills out TFC form with their concerns and provides it to Veoneer
Initial Feasibility Study@ supplier
Start TFC Process
TFC process initiated either by RFQ or by other Serial Change
Explanation
If a show stopper is identified a Pre-Sourcing Initial TFC review with Supplier & Veoneer needed
CLD 3 - Detailed review TFC Meeting with Supplier & Veoneer is needed before sourcing decision
Process Flow
TFC evaluation @ Veoneer
Sourcing decision@ Veoneer
Each concern must state a clear action plan, addressed responsible persons as well as due dates.
ORDER SHALL NOT BE ISSUED WITHOUT AN AGREED & SIGNED TFC
After tool order, before PPAP: Implementation & follow up of all in TFC agreed actions
Final TFC review: All open issues closed prior to PPAP Submission (PPAP Package Creation and PSW Submission)
PPAP approval
PPAP WILL NOT BE APPROVED WITHOUT COMPLETED TFC.
Person in charge &
Phase
Project / Serial buyer
Sourcing Phase
Project / Serial Buyer
Tool Order Phase
SQ
SQP Phase
Notes: Shown here is a flow chart of the TFC process.

## Slide 8: TFC flow chart
TFC meeting / call
supplier & Veoneer
Tool order /
order of design change
TFC follow up
TFC closure meeting/ call with supplier
Supplier fills out TFC form with their concerns and provides it to Veoneer
Initial Feasibility Study@ supplier
Start TFC Process
TFC process initiated either by RFQ or by other Serial Change
Explanation
If a show stopper is identified a Pre-Sourcing Initial TFC review with Supplier & Veoneer needed
CLD 3 - Detailed review TFC Meeting with Supplier & Veoneer is needed before sourcing decision
Process Flow
TFC evaluation @ Veoneer
Sourcing decision@ Veoneer
Each concern must state a clear action plan, addressed responsible persons as well as due dates.
ORDER SHALL NOT BE ISSUED WITHOUT AN AGREED & SIGNED TFC
After tool order, before PPAP: Implementation & follow up of all in TFC agreed actions
Final TFC review: All open issues closed prior to PPAP Submission (PPAP Package Creation and PSW Submission)
PPAP approval
PPAP WILL NOT BE APPROVED WITHOUT COMPLETED TFC.
Person in charge &
Phase
Project / Serial buyer
Sourcing Phase
Project / Serial Buyer
Tool Order Phase
SQ
SQP Phase
000
001
002
Notes: The TFC process is initiated by either an RFQ or an SREA from a supplier.
Purchasing facilitates the TFC effort in the Sourcing and Tool Order Phases. SQ facilitates the SQP Phase.
In the sourcing phase the TFC is automatically generated and attached in PLM by an RFQ in E-sourcing. Purchasing reviews TFC looking for Showstoppers.
If significant issues are identified or the CLD is a CLD 3 a detailed TFC review is needed with the supplier prior to sourcing.
In the Tool Order Phase a detailed review with the supplier is to be held to identify and agree clear actions for each issue. A tool order will not be issued without agreed actions between Veoneer and the supplier.
In the SQP phase the SQ tracks with CTF support the completion of all actions. Full PPAP approval will not be granted if all actions are not complete.
As a quick note on TFC document control.
A TFC is released in PLM for each phase. In the Sourcing Phase the TFC 000 revision is released with supplier issues and proposed actions.
In the Tool Order Phase the TFC 001 revision is released with agreed actions.
In the SQP Phase the TFC 002 revision is released showing all actions complete.
TFC E document approval is signed by the supplier and Veoneer (either purchasing or SQ) in PLM or in the supplier Portal for the supplier.

## Slide 9: TFC
Review each “note” and “dimensions” from drawing for concerns
Must review Checklist items against each drawing requirement
Check measurability for each characteristic
Proactively suggest solutions for each concern identified
Suggest improvements for more robust production (quality and efficiency)
Promote open and honest communication with Veoneer
  Address issues/concerns as soon as possible
  Response in a timely manner to achieve project milestones
Supplier responsible to meet agreed timing
Expectations towards Suppliers
Notes: In order to achieve a successful component part launch here is summary of the supplier expectations.
Supplier must review each note and dimension on the drawing.
The supplier must review the checklist against the component design at the latest in the start of the Tool Order Phase . They need to indicate on the checklist tab that each item has been evaluated.
Must be able to measure that part against the drawing
This is an opportunity to suggest improvements toward quality, manufacturability and cost.
The TFC process should promote open and honest communication with Veoneer. The earlier we hold the TFC reviews the more capable we become to mitigate risk.
The supplier is responsible to meet timing or raise timing concerns early.
It is important for both Veoneer and the Supplier that no one takes short cuts and that we communicate clearly to ensure a successful Launch so that we satisfy Veoneer’s customers to continue to win more business by being the best in the industry.

## Slide 10: TFC Training
Template details

## Slide 11: TFC Purpose
Purpose for TFC process is to get commitment from supplier and Veoneer cross functional team regarding feasibility in manufacturability, quality, packaging definition and timing in order to minimize any risk and cost avoidance upfront.
  Create/Complete actions to agree on a drawing and measurement method for tool kick off
  Target for supplier to provide parts 100% to drawing at PPAP submission on-time
TFC required for each new part or serial part revision change (e.g. 612345600A to 612345600B)
Notes: The TFC purpose is for the Cross Functional Team (CFT) to evaluate with the supplier each part drawing for feasibility of manufacture, Quality, Packaging definition and timing to mitigate launch risk as early as possible.
Or in other words complete agreed actions on a drawing and measurement method so that production tooling can be kicked off so that the supplier can provide parts and obtain full PPAP on-time.
A new TFC is required for each new part or part major revision change. This is supported by the integration of the TFC in the E-sourcing system.

## Slide 12: Understanding the TFC template
Sections
9
1
2
3
4
6
8
5
7
Notes: We will now review each section of the TFC template with details of how it is to be fill out properly.

## Slide 13: Understanding the TFC template
Section 1
  Part Name:
  Add Part name, stated on drawing
  Populated from RFQ
  Drawing No. / Specification:
  State Drawing Number or Specification this TFC is referring to
  Populated from RFQ
  Veoneer Input: Information provided by Veoneer
  Drawing Revision:
  State Drawing Revision as stated on drawing this TFC is referring to
  Populated from RFQ
  In case of not released drawing, state receipt date of drawing
  In case of hand released drawing, state comment “hand released on” and date of signature
  Part Number:
  State Part Number as listed on drawing this TFC is referring to (including the letter index)
  Populated from RFQ
  Requester Name/Date:
  State Name and Date of TFC requester
  Populated from RFQ (Owner)
Veoneer Input | 
Part Name | PCB, RF,77GHZ,1.2 AD LDO AM TX3, 2.0WL TX
Drawing No. / Specification | 680146000A / MS6001 / ECAD E8011300
Drawing Revision | 000
Part Number | 680146000A
Requester Name/Date | Thomas Werner 30/01/2019
Notes: Section 1 is automatically populated from the E-sourcing application when an RFQ is created.
As a side note this is another good reason why we should quote released part numbers instead of E sketches.
Items include:
Part name
Drawing number and revision
Part number
And the TFC requester which is the RFQ Owner

## Slide 14: Understanding the TFC template
Section 2
  Supplier(s) of Raw Material:
  State all Supplier(s) of required Raw Material
  Supplier (Name & ID):
  State name and given Veoneer supplier ID of supplier facility, which will be providing the PPAP documentation.
  Populated from RFQ
  If not available, please contact responsible Veoneer Lead buyer or TFC Requester.
  Supplier Manufacturing Location:
  State location of physical production of referred Part
  Supplier Input: Information should be available within supplier company
  Raw Material(s):
  State all Raw material(s) which will be required to manufacture referred Part.
  Tool Maker Name:
  State (Company) Name of Tool manufacturer.
  Put n/a if no new tools are manufactured
Supplier Input | 
Supplier (Name & ID) | Schweizer Electronic AG / WUS Kunshan , ID.862085
Supplier Manufacturing Location | Kunshan
Tool Maker Name | n/a
Raw Material(s) | Isola
Supplier(s) of Raw Material | Material 185HR+ , ASTRAMT772 0.127D X018X035
Notes: Section 2 is the key supplier information.
It includes:
Supplier Name and ID. This field is populated automatically from the RFQ.
The remaining fields in this section are to be filled out manually by the supplier
Supplier location
Tool maker name
Raw materials used in component
Suppliers of the raw materials

## Slide 15: Understanding the TFC template
Section 3
  TFC PLM “E” No.:
  State PLM E Number where this TFC is stored.
  Will be provided by Veoneer
  Populated from RFQ
  TFC Revision No./Date:
  State revision number and date of TFC.
  Increase No., whenever TFC is shared and modified, to ensure a proper traceability.
  Populated from RFQ
  TFC Revision Information: General Information of TFC, mandatory for traceability and proper documentation.
  Tool Asset No.:
  State producing Tool Asset No. as tagged on the tool, provided via Tool contract or provided by Veoneer colleagues.
  (When applicable)
TFC Revision Information | 
TFC PLM "E" No.: | E8024838
TFC Revision No./Date | 000 / 2018-11-19
Tool Asset No. | n/a
Notes: Section 3 is the TFC revision information.
The TFC PLM E number and revision number and date are auto populated by the E-sourcing RFQ.
The tool asset number is optional and is a manual entry field.

## Slide 16: Understanding the TFC template
Section 4
Supplier Feasibility Statement | 
Yes w/Actions | Design Feasible (PPAP without any deviations)
YES | Feasibility has been assessed against the criteria listed in the Checklist (Deviations list in below in actions)
  Feasibility has been assessed against criteria listed in Checklist (Deviations list in below in actions): Drop Down:
  Design shall be assessed against all items listed in “Checklist” (see also Section 9)
  NO
  Design has not been assessed against criteria. Order shall not be sent
  YES
  Design has been assessed against criteria. All Deviations shall be stated in action list (see also Section 7)
  Supplier Feasibility Statement: Overall TFC statement and confirmation given by supplier.
  Design Feasible (PPAP without any deviations: Drop Down:
  Clearly state feasibility of referred drawing
  NO
  Design is not feasible
  YES
  Design is feasible without any limitations
  Yes w/Actions
  Design is feasible without any limitations if actions as stated below are completed prior to PPAP submission
Notes: Section 4 is where the supplier declares the feasibility status of the part and drawing.
The first declaration for the “Design Feasible (PPAP without any deviation) has the following options:
“No” which means there are show stoppers and the part cannot be produced as designed. This option will highlight the field RED.
“Yes” which means the design is feasible without concerns. Field highlight is GREEN.
“Yes w/actions” indicates that there are not any showstoppers but there are concerns than need to be addressed with actions. This will highlight the field YELLOW.
The second declaration for Feasibility has been assessed against the criteria listed in the Checklist and has two options
“No” the design has not been reviewed against the checklist criteria and the field is highlighted in RED
“Yes” the design has been reviewed against the checklist and the field is highlighted GREEN

## Slide 17: Understanding the TFC template
Section 5
  Timing: Major Timings related to affected project
  (When Applicable)
  Tool Order:
  (Expected) Tool Order date – Official PO
  First Off Tool:
  Veoneer receipt date of First Off Tool Parts.
  Populated from RFQ
  To be agreed before PO if First Off Tool parts shall be submitted or Functional OK parts are required
  Supplier 1st Production Trial Run (PTR):
  Date of first production Run performed at supplier serial plant
  PPAP Submission:
  Date of Veoneer receipt Date of complete PPAP documentation including PPAP parts (if applicable).
  Populated from RFQ
  PPAP to be submitted without any deviations and TFC status “completed” mandatory.
  Veoneer SOP:
  Date of Start of Production.
  Populated from RFQ
  PPAP needs to be approved prior to this date.
  Supplier SOP:
  Date of Start of Production.
  PPAP needs to be approved prior to this date.
Timing | Date | Timing | Date
Tool Order | Nov.,2018 | Supplier 1st Production Trial Run (PTR) | TBD.
First Off Tool | Dec.,2018 | PPAP Submission | Jan.,2019
Veoneer SOP | Jan.,2020 | Supplier SOP | TBD.
Notes: Section 5 is the timing section. It is important that we understand the feasibility of the supplier meeting the project timing.
The Tool Order date is the date that Veoneer expects to issue the tooling Order. It is provided by the Buyer as agreed with the cross functional team.
The First off tool date is when first off tool parts are required at Veoneer. It is auto populated from the E-sourcing RFQ.
The Veoneer SOP is also auto populated from the RFQ and represents the date that the Veoneer production site will start production.
The Supplier first production trial run or PTR is filled in by the supplier.
The PPAP Submission date is auto populated from the RFQ and represents the date that the supplier shall submit the PPAP to Veoneer.
The Supplier SOP data is also filled in by the supplier. PPAP should be approved by this date.

## Slide 18: Understanding the TFC template
Section 6
  Part Image: Insert picture of referred Part
  (Recommended)
Notes: Section 6 is a space to paste a picture of the part from the drawing or model. We find this a helpful reference.

## Slide 19: Understanding the TFC template
Section 7
Row No. | Drawing Reference | Concerns (Specification, Checklist or Other) | Actions (Each concern must have an assigned proposal for solution from the supplier and then an agreed action with Veoneer) | Veoneer | Supplier | Person Responsible | Target Date | Status
1 | Blind holes (D0.65mm) | You defined the tolerance of D0.65mm blind holes as +/-0.08mm in drawing. To meet the minimum the distance between hole wall and hole wall as 0.40mm, Wus has to use Dia 0.65mm drill bit for them. | Wus will use drill bit size as D0.65mm for these blind holes, So please release the tolerance from Dia0.65+/-0.08mm to Dia0.65+0.08/-0.15mm. Please confirm. | x |  | Weichun Chang | 30/01/2019 | COMPLETE
2 | Stackup | As att1 shown,you define the stackup as below,and control the board thickness as 1.45mm+/-10% including copper excluding solder mask. | Wus suggestion is listed as below. 1)You do not define the FR4,we suggest to use the base material 185HR (TG 170) .Please confirm. 2)We suggest to stackup (which shown in att1 sheet) ,and control the total board thickness as 1.45mm+/-10% including copper and solder mask.Please confirm. | x |  | Weichun Chang | 30/01/2019 | COMPLETE
3 | Impedance | It is required to control the impedance as att1 shown,but we can not meet it. | Now we suggest to adjust some trace width as att1 shown to meet the impedance.Please confirm. | x |  | Weichun Chang | 30/01/2019 | COMPLETE
  Person Responsible:
  Clearly state name of a single person who is responsible for mentioned action. General names (departments, company name) are not acceptable.
  Target Date:
  State Target Date agreed Actions will be complete.
  Veoneer:
  Put a “x” if Veoneer person is responsible for completing mentioned action.
  Actions:
  Clearly state a feasible action in order to close mentioned issue. Cell should be pre-filled by TFC sender (e.g. Supplier). Responses to proposal are added to end of the cell text (e.g. agreement, Rejection or counter proposal)
  All mentioned actions shall be completed prior to PPAP submission. All mentioned activities shall have a clear follow up (e.g. If result is A then Action A, if result is B then Action B). Open actions without clear follow-up are not acceptable (e.g. FOT parts needs to be investigated)
  Do not delete any concerns retain history of actions.
  Row Number:
  Running number for reference purpose. Each line within this section shall contain one number for better identification and reference.
  Drawing Reference:
  State clear reference number as stated on drawing or checklist Item, concern is referring to.
  If concern is not referring to a specific Drawing Reference or Checklist item, put short and clear explanation.
  Concerns:
  Clearly state concern; what is issue and why it is not feasible to fulfill specific request.
  Supplier:
  Put a “x” if Supplier person is responsible for completing mentioned action.
  Status: Drop Down:
  State Status of listed Actions
  PROPOSED: Actions are proposed and not yet agreed with
  all involved Parties
  AGREED: Actions are agreed, but not yet performed and completed.
  COMPLETE: Actions have been fully performed and no
  further activities needs to be done for specific concern.
  REJECTED: Actions have been rejected
Notes: Section 7 is the meat of the TFC document. This is were feasibility concerns are documented by the supplier with their proposed actions. Then the Veoneer team and supplier document the agreement to address the concerns and track them to closure.
The Row number column is only an aid in identification for referencing issues and is a manual entry field.
In the Drawing reference field the supplier enters the Drawing note, dimension number or checklist number that is in question.
In the Concerns field they state the concern with the item.
The Actions field is a working field. First the supplier enters their recommendation. Then between Veoneer and the supplier the agreed action is documented.
The next two fields are to identify if the responsibility of the action is Veoneer or the supplier. Just enter an “X” in the appropriate column.
The person responsible field is where the team clearly states a single person as responsible for the action. Multiple names or general function names are not allowed.
Veoneer and the supplier should document the agreed target date for action completion in this field.
The status field is an indicator of what state the action is in. The text is highlighted based on selected status. When the supplier first generates the TFC they should select proposed which is highlighted Orange. Once Veoneer and the supplier have agreed on an action then the status should be changed to Agreed the cell is changed to Yellow. When the action is complete then the status should be changed to Complete and the cell is colored Green.

## Slide 20: Understanding the TFC template
Section 8
Veoneer Representatives |  | Supplier Representatives |  | 
Function | Name | Function |  | Name
Design Engineer | Weichun Chang |  |  | 
Project SQ | Forest Song |  |  | 
Project Buyer | Thomas Werner | Account Manager | Carsten Schimanke | 
  Function:
  State function of involved Supplier employee.
  Supplier - Representative(s) (covering functions: Engineering, Tooling, Quality, Account Management, Sales)
  Veoneer Representatives:
  Involved People from Veonerr in referred TFC discussion.
  Supplier Representatives:
  Involved People from Supplier side in referred TFC discussion.
  Function:
  State function of involved Veoneer colleague.
  Name:
  State clear name of involved Veoneer colleague.
  Name:
  State clear name of involved Supplier employee.
Notes: Section 8 is a place to document participants from both Veoneer and the Supplier.
Actual approvals are now part of PLM. The TFC E document number is approved by an Veoneer SQ and then approved by the supplier via the Veoneer Partner Portal connection to PLM. The approval and revision process will be further explained in a few more slides.

## Slide 21: Understanding the TFC template
Section 9
  Checklist:
  2nd sheet of TFC File. Each Item (CL1 - CL22) needs to be checked and evaluated for each new drawing revision and project.
  Each deviation (status red) needs to be stated in 1st sheet of TFC file.
  Input and review of the Status is not needed in Sourcing Phase but shall be done in Tool Ordering Phase.
  TFC Proposal:
  1st sheet of TFC file.
  Needs to be filled for each new Drawing Revision and each project.
TFC Evaluation Checklist |  | 
Checklist Item # | Evaluation Criteria | Evaluated
CL1 | Component Timing (Is the timing listed on TFC Proposal Sheet feasible?) | Evaluated
CL2 | Master PFMEA Considerations (Are there any concerns from the Master PFMEA?) | Evaluated
CL3 | Referenced Documents (Are all specifications, standards Master Drawing for GPM application parts and requirements referenced in the drawing, OEM requirements and other requirements known, understood and available?) | Evaluated
CL4 | Dimensions & Tolerances, Form, Location Characteristics, Remarks and Annual Layout Inspection (Are tolerances for all positions and requests on drawing clearly defined? Note tolerances that are not achieveable in section below.) | Evaluated
CL5 | CAD Model (Are all the contours feasible for robust tool design and producible in tool?) | Evaluated
CL6 | Marking (Is the marking of the part feasible as described in the drawing/specification?) | Evaluated
CL7 | Material Specifications (Are all positions and requests considered such as material name, material standards, elongation, flammability, availability, etc? Is the material suitable to fulfill the requirements?) | Evaluated
CL8 | Functional, Performance and Reliability Specifications (Are all positions and requests considered, e.g., form stability, tensile strength, assembly force, must fit part xy, durability?) | Evaluated
CL9 | Surface Treatment Requirements (Related to parts not tool) (Are coating, painting, polishing Heat Treatment, etc., of parts clearly specified and achievable?) | Evaluated
Notes: Section 9 is the checklist tab. The Checklist has 22 evaluation categories that the component part needs to be evaluated against. This list is based on Lessons Learned and corrective actions at Veoneer.
The Checklist is not required to have been evaluate in the sourcing phase but is recommended.
The Checklist is required to be used for evaluation by the supplier and documented on the checklist tab in the Tool order phase.
The options for the checklist include:
Not Evaluated which is the default option.
And Evaluated which means that the checklist item number has been considered against the launch part requirements.

## Slide 22: TFC template
Notes: Here is a screen shot of the new TFC template filled out. Also shown is the checklist that the supplier is to evaluate the component against for feasibility.
Key items for the template.
Veoneer should provide the key timing dates such as tool order, first off parts, PPAP submission and Veoneer SOP (the supplier can get these dates from the RFQ) However, First off Part, PPAP submission and Veoneer SOP are automatically populated in the TFC template from the E-sourcing RFQ.
Suppliers are not required to review in detail the checklist during the Sourcing phase but must review in the Tool order phase.
The supplier must make a declaration of whether the design is feasible to PPAP without any deviations. They must also make a declaration that the design has been evaluated against the Checklist criteria.
Each issue identified by the supplier should have a recommended action and the status changed to proposed. Once the Detailed review meeting is held and agreement of actions made between Veoneer and the supplier the status should be changed to Agreed. Upon completion of actions the status is to be changed to Complete.

## Slide 23
TFC Flow chart PLM Document flow
Notes: The finial item that we will review is the PLM Document Approval process
The TFC is automatically generated by an E-sourcing RFQ or needs to be manually created in PLM if initiated by an SREA.
The 000 revision in where the supplier first documents their concerns. This version is released in PLM without further input automatically upon supplier award in E-sourcing.
The 001 revision is created and agreed actions between the supplier and Veoneer are documents. Upon agreement the TFC 001 is released. Then the 002 revision is created to document the completion of the agreed actions. Once ALL actions are complete the 002 revision is released. The released 002 revision is then manually linked to the appropriate SQP.

## Slide 24: Thank You!
Notes: Thank you for watching this TFC Training.